## Slide 1: Graduation Project
Structural Design of Technology College in
Hebron University
Prepared By :
  Ra’ef Noor
  Abd Al-Lateef Sbaih
  Mohamed Hamdan
An-Najah National
University
Engineering College
Civil Engineering
Department
2011
Supervised By:
  Ins. Ibrahim Araman

## Slide 2: PROJECT DEFINITION
This project will introduce the structural analysis and design of the building of “Hebron University for Technological Sciences” which is located in Hebron.

## Slide 3: PROJECT Description
This building consists of 8 stories with about 1500m2 area for each floor .
The building is about 76m long.
The building will be separated using expansion.
It consists of a parking floor then seven typical floors.
From a structural point of view the structural
elements, footings, columns, beams, and slabs will be
designed by hand and then using SAP2000.
Codes & standards
ACI318-08 .
IBC-2009.
UBC-97.

## Slide 4
Live an Superimposed dead loads as follow :
  Live Load were considered to be 5KN/m2
  Superimposed were calculated and considered to be 4KN/m2.
lOADS
Materials
B300 Concrete (f’c=24MPa, E=2.33x107 KN/m2).
B400 Concrete (f’c = 32MPa, E= 2.66x108 KN/m2) for columns.
Unit weight of reinforced concrete = 24.5 KN/m2
Steel Grade 60 ( Fy= 420 MPa , E= 200GPa)
Soil Bearing Capacity = 500 KN/m2

## Slide 5
The Structural system were a combination of moment resisting frames mixed with shear walls.
As the building has a relatively long spans varies from 6.2 to 11 meters, the slabs system was a combination of one-way and two-way solid slabs with interior beams.
The Structural System

## Slide 6: Plan

## Slide 7
Preliminary Dimensions
Slabs
1-Way Solid slabs

## Slide 8
Preliminary Dimensions
Slabs
2-Way Solid slabs
h =
h =

## Slide 9: Design frame sample

## Slide 10
For the sample frame mentioned before beams [650x600] mm will be used.
523mm
H =
Use , 600mm depth
Preliminary Dimensions
Beams

## Slide 11
Preliminary Dimensions
Columns
Tributary area for column B-4 = 8.2 x 8.65 = 70.93m2
Total loading = 1.2 x (6. 25+4) + 1.6 x 5= 20.3 KN/m2
Axial load on column B-4 =20.3 (KN/m2) x 70.93 (m2) x 8 =11520 KN
Considering it as a short column,
Ag = 9882cm2 , Use 100x100cm.

## Slide 12: 3d mODEL

## Slide 13
Structural Model Verification
Check Equilibrium.
Loads : | Manual | SAP | % Err
LL = | 40121 KN | 39951 KN | 0.43%
SIDL = | 44429.7 KN | 43564.0 KN | 1.99%

## Slide 14
Compatibility Check

## Slide 15
Modifiers

## Slide 16
Seismic Coefficients
Seismic Coefficient Ca = 0.15
Zone factor, Z = 0.15
Seismic Coefficient Cv = 0.15
Since, B.C = 500 KN/M2
The Soil Profile Coefficient is SB
Response Spectrum Scale Factor =
Importance factor = I = 1.25
g = 9.81 m/sec2
Over strength factor, R = 5.5
Response Spectrum factor = 2.23

## Slide 17: Design of Slabs
As slab thickness were determined in Chapter 2, a deflection and strength check will be performed to assure the suitability of the dimensions.
Max span in the building is 11m , so
  Max deflection allowed from D+L = = 61.1mm

## Slide 18: Design of Slabs
  Max deflection allowed from L only = = 45.8mm

## Slide 19
Flexure Design :
Minimum reinforcement of slab = 0.0018 x b x h = 0.0018 x 1000 x 2500 = 450mm2
Use, 1φ12/250mm (Actual Area = 452mm2)
For slab 250mm.
Md = φMn === 33404281 N.mm/m
Md = 33.4 KNm/m, this is the minimum capacity of min steel
M11 Positive Moment ( Max Envelope between Range -33 to +33KNm/m )

## Slide 20
Flexure Design :
M11 Negative Moment ( Max Envelope between Range -33 to +33KNm/m )
M22 Positive Moment ( Max Envelope between Range -33 to +33KNm/m )

## Slide 21
M22 Negative Moment ( Min Envelope between Range -33 to +33KNm/m )
Max moment (KN.m) |  | Strip (mm) | Moment KN.m/m | Thickness H(mm) | ρ | ρmin | As (mm2) | Use |  |  |  | Spacing
-ve | 39 | 1750 | 22.29 | 250 | 0.00101 | 0.00180 | 360 | 4 | φ | 12 | /m | 25.0
+ve | 155 | 3800 | 40.79 | 250 | 0.00186 | 0.00180 | 466 | 4 | φ | 14 | /m | 25.0
-ve | 271 | 3800 | 71.32 | 250 | 0.00331 | 0.00180 | 827 | 4 | φ | 18 | /m | 25.0
+ve | 93 | 3800 | 24.47 | 250 | 0.00111 | 0.00180 | 360 | 4 | φ | 12 | /m | 25.0
-ve | 274 | 3800 | 72.11 | 250 | 0.00335 | 0.00180 | 837 | 4 | φ | 18 | /m | 25.0
+ve | 173 | 3900 | 44.36 | 250 | 0.00203 | 0.00180 | 508 | 4 | φ | 14 | /m | 25.0
-ve | 46 | 3800 | 12.11 | 250 | 0.00055 | 0.00180 | 360 | 4 | φ | 12 | /m | 25.0
M11 Design :

## Slide 22
Wide-Beam Shear:
Shear Force contours in V13 (KN/m)
= 122474.5N = 122.5 KN/m
=

## Slide 23: Design of Beams
Rebar Percentage
Longitudinal Flexure Steel in mm2
Torsion Reinforcement ( Alin mm2, and At/s in mm2/mm)

## Slide 24
Torsion Reinforcement ( Alin mm2, and At/s in mm2/mm)
Shear Reinforcement ( Av/s in mm2/mm)

## Slide 25: Design of Columns
=
Columns rebar ratios should be kept under 2% for ductility requirement for seismic design in Chapter 21.
Column shear reinforcement are minimum
because the shear force is much smaller than
the shear capacity of the section.
 |  | Part A - Building |  |  |  |  |  |  |  |  | 
 |  | C1 |  | C2 |  | C3 |  | C4 |  | C5 | 
Basement | Dims | 75 | 75 | 75 | 75 | 90 | 90 | 95 | 95 | 25 | 50
 | As | 5625 |  | 5625 |  | 9442 |  | 17115 |  | 1250 | 
 | Reinf. | 23 | φ 18 | 23 | φ 18 | 25 | φ 22 | 22 | φ 32 | 12 | φ 12
 | Ties | Φ10 @ 250 |  | Φ10 @ 250 |  | Φ10 @ 250 |  | Φ10 @ 250 |  | Φ10 @ 250 | 
Typical Floor | Dims | 75 | 75 | 75 | 75 | 90 | 90 | 95 | 95 | 25 | 50
 | As | 5625 |  | 5625 |  | 8100 |  | 9025 |  | 1250 | 
 | Reinf. | 23 | φ 18 | 23 | φ 18 | 22 | φ 22 | 24 | φ 22 | 12 | φ 12
 | Ties | Φ10 @ 250 |  | Φ10 @ 250 |  | Φ10 @ 250 |  | Φ10 @ 250 |  | Φ10 @ 250 | 
Last Floor | Dims | 75 | 75 | 75 | 75 | 90 | 90 | 95 | 95 | 25 | 50
 | As | 5625 |  | 12816 |  | 9851 |  | 9025 |  | 1250 | 
 | Reinf. | 23 | φ 18 | 27 | φ 25 | 26 | φ 22 | 24 | φ 22 | 12 | φ 12
 | Ties | Φ10 @ 250 |  | Φ10 | @ 250 | Φ10 | @ 250 | Φ10 | @ 250 | Φ10 | @ 250

## Slide 26: Design of Columns
=
Stirrups :
Spacing between stirrups along the column except the ends is the least of:
  16 db= 16 x 18 = 288mm (Controls)
  48 ds =48 x 10 = 480mm
  Least column dimension = 950mm
The spacing between stirrups, So,distributed over length Lomeasured from the
face of support shall not exceed the smallest of:
  8 x Smallest bar diameter = 8 x 18 = 144mm
  24 x Hoop diameter = 24 x 10 = 240mm
  One-half of the smallest dimension = 450mm
  300mm
  So, So= 144mm
length Lomeasured from the face of support which shall not be less than the
largest of :
  One-sixth clear span of column = 630mm
  Max dimension = 950mm
  450mm
  So, Lo = 630mm

## Slide 27: Design of Stairs
=
As stair should be a safe escape root for the residents in the buildings , a slight increase in the loads will be used. This is a public building with 5 KN/m2, therefore 7 KN/m2will be used on stairs .
Max span here is 4m so the required depth is 200mm
As min = 0.0018 x b x h = 0.0018 x 1000 x 200 = 450mm2
Use, 1φ12/250mm (Actual Area = 452mm2)
For slab 200mm.
Md = 24.85 KNm/m ,
this is the minimum capacity of min steel.
200m

## Slide 28
M11 Positive Moments
M11 Negative Moments
M22 Positive Moments
M22 Negative Moments
Bending Moments in the stairs.

## Slide 29
Design of footings
Isolated Footings Dimensions ;
4.46m2
6.2m2
Depth of the Sample footing;
Assume d =600mm

## Slide 30
Design of footings
Group-Max Ultimate Load | Foot-ID | Dims | Depth | X-Dir Steel |  |  |  | Y-Dir Steel |  |  |  | Shrinkage* |  |  | 
629 | F1 | 1.5 x 1.5 | 0.6 | 1 | ɸ | 20 | / 20 | 1 | ɸ | 20 | / 20 | 1 | ɸ | 12 | / 40
2596 | F2 | 2 x 2 | 0.5 | 1 | ɸ | 16 | / 15 | 1 | ɸ | 16 | / 15 | 1 | ɸ | 12 | /40
4404 | F3 | 2.5 x 2.5 | 0.6 | 1 | ɸ | 18 | / 15 | 1 | ɸ | 18 | / 15 | 1 | ɸ | 12 | / 40
4795 | F4 | 3 x 3 | 0.7 | 1 | ɸ | 18 | / 15 | 1 | ɸ | 18 | / 15 | 1 | ɸ | 12 | / 40
6785 | F5 | 3.5 x 3.5 | 0.8 | 1 | ɸ | 20 | / 15 | 1 | ɸ | 20 | / 15 | 1 | ɸ | 12 | / 40
8116 | F6 | 4 x 4 | 0.95 | 1 | ɸ | 20 | / 15 | 1 | ɸ | 20 | / 15 | 1 | ɸ | 12 | / 40
12674 | F7 | 4.5 x 4.5 | 1.15 | 1 | ɸ | 20 | / 15 | 1 | ɸ | 20 | / 15 | 1 | ɸ | 12 | / 40
15532 | F8 | 5 x 5 | 1.35 | 1 | ɸ | 25 | / 20 | 1 | ɸ | 25 | / 20 | 1 | ɸ | 12 | / 40

## Slide 31
Design of combined footing

## Slide 32
Depth of combined footing

## Slide 33
Design of Wall footing - Basement
P service max( from Gravity and seismic load) =4403/2.9=1525 KN/m.
Pu =6345.8/2.9=2193 KN/m
Ultimate moment max( from Gravity and seismic load)=50 KN.m
B = 2.34 m2, Let B=2.4 m

## Slide 34
Design of Wall footing - Basement
 | Footing ID | Width (cm) | Depth | X-Dir Steel | Y-Dir Steel | Shrinkage
Part A | Stair Wall Footing | 220 | 60 | 6φ20 /m | 6φ16 /m | 6φ14 /m
 | Typical Wall Footing | 140 | 45 | 6φ18 /m | 6φ14 /m | 6φ14 /m
Part B | Typical Wall Footing | 250 | 60 | 6φ18 /m | 6φ14 /m | 6φ14 /m

## Slide 35
Thanks you for listening so attentively